## Slide 1: Analysis of Functional Magnetic Resonance Imaging (fMRI) Image Preprocessing 李宜恬 Yi-Tien Li, Ph.D. TMU Neuroscience Research Center, Taipei Medical University Translational Imaging Research Center, Taipei Medical University Hospital angela810727@tmu.edu.tw July 28th , 2022

## Slide 2: Employed Software
RadiAnt DICOM Viewer
  https://www.radiantviewer.com/
Statistical Parametric Mapping (SPM 12)
  http://www.fil.ion.ucl.ac.uk/spm/
dcm2niigui
  https://drive.google.com/file/d/1vNBcJnIVMgXBfSIndNf0bEDT7_Z5yRQf/view?usp=sharing

## Slide 3: DICOM (1993)
Digital Imaging and COmmunication in Medicine
  The common language of medical equipment
  Retrieve of subject/imaging information
DICOM tags (header)
DICOM images
+

## Slide 4: DICOM Import
DICOM format (*.dcm, *.ima, *. ) → NIfTI (*.nii)
DICOM image folder
Compressed DICOM

## Slide 5: DICOM Import
DICOM format (*.dcm, *.ima, *. ) → NIfTI (*.nii)
dcm2niigui
DICOM image folder

## Slide 6: DICOM Import
DICOM format (*.dcm, *.ima, *. ) → NIfTI (*.nii)
DICOM image folder

## Slide 7: DICOM Import
DICOM format (*.dcm, *.ima, *. ) → NIfTI (*.nii)
DICOM image folder

## Slide 8: fMRI Protocol (see DICOM tags)
DICOM image folder
RadiANT DICOM Viewer (64-bit)

## Slide 9: fMRI Protocol (see DICOM tags)
(0008,0070) Manufacturer : SIEMENS
(0018,0087) Magnetic Field Strength : 3 (T)
(0008,1090) Manufacturer’s Model Name : Prisma
(0018,0024) Sequence Name : *epfid2d1_70 →2D GRE EPI
(0018,0080) Repetition Time : 2000 (ms)
(0018,0081) Echo Time : 20 (ms)
(0018,1314) Flip Angle : 90 (°)
(0028,0030) Pixel Spacing : 3\3 (mm)
(0028,0010) Rows : 64
(0028,0011) Column : 64
(0018,0088) Spacing Between Slices : 3.5 (mm)
(0018,0050) Slice Thickness : 3.5 (mm)
(0019,100A) Number of Image in Mosaic : 40 (slices)
BOLD fMRI images (Moisaics)

## Slide 10: Set up
Matlab
R2020a
Set Path > Add with Subfolders… > spm12 > 選擇資料夾

## Slide 11: Set up
Matlab
R2020a
Set Path > Add with Subfolders… > spm12 > 選擇資料夾 > Save > Close

## Slide 12: Analysis of Functional Magnetic Resonance Imaging (fMRI) Set up SPM12 Batch Parameters

## Slide 13: Preprocessing Procedure
Slice Timing Correction
Realignment
Segmentation
Co-registration
Normalization
Smooth
Output :
a*.nii
ra*.nii
mean*.nii
rp_*.txt (head motion log)
c1*.nii, c2*.nii, c3*.nii, c4*.nii, c5*.nii
m*.nii (bias corrected T1W)
y_*.nii (deformation field)
wra*.nii
swra*.nii
Input :
20*.nii (EPI)
a*.nii
20*.nii (T1W)
ra*.nii
mean*.nii
m*.nii
m*.nii
ra*.nii
y_*.nii
wra*.nii
*(Opts)

## Slide 14: Batch of fMRI preprocessing
>> spm fmri
> Batch
> fMRI_preprocessing_batch_YTLi20210112.mat
> Done

## Slide 15: Batch of fMRI preprocessing
>> spm fmri
> Batch
> fMRI_preprocessing_batch_YTLi20210112.mat
> Done

## Slide 16: Batch of fMRI preprocessing
> Select the SPM Tissue Probability Map (~\spm12\TPM.nii)
→ TPM.nii,1
→ TPM.nii,2

## Slide 17: Batch of fMRI preprocessing
> Select the SPM Tissue Probability Map (~\spm12\TPM.nii)
→ TPM.nii,4
→ TPM.nii,5
→ TPM.nii,6

## Slide 18: Batch of fMRI preprocessing
→ TPM.nii,4
→ TPM.nii,5
→ TPM.nii,6
> Save new batch file

## Slide 19: Batch of fMRI preprocessing
> Select files for preprocessing
Data folder
~\HC003_20160620_CYJ\MRIData\WM1
T1 files
~\HC003_20160620_CYJ\MRIData\T1\20*.nii
(1 volumes)
fMRI files
~\HC003_20160620_CYJ\MRIData\WM1\20*.nii
(105 volume)

## Slide 20: Slice Timing Correction
Slice Timing Correction
Realignment
Segmentation
Co-registration
Normalization
Smooth
Correct for temporal offset between slices for multi-slice acquisition
Interleaved Acquisition
temporal interpolation

## Slide 21: Slice Timing Correction
Slice Timing Correction
Realignment
Segmentation
Co-registration
Normalization
Smooth
Sessions : ~\HC003_20160620_CYJ\MRIData\WM1\20*.nii
(105 fMRI volumes)
Number of Slices : (0019,100A) Number of Image in Mosaic : 40
TR : (0018,0080) Repetition Time : 2000 (ms) → 2 (s)
TA : TR-TR/Number of Slices → 2-2/40 = 1.95
Slice order : 2:2:40 1:2:39 → SIEMENS interleave acquisition
Reference Slice : 2 → SIEMENS interleave acquisition
Filename Prefix: create a*.nii files after this step

## Slide 22: Realignment (Head motion correction)
Slice Timing Correction
Realignment
Segmentation
Co-registration
Normalization
Smooth
The signal variation from head movement is much larger than hemodynamic response.
…
…
t = 0
t = 2
t = 4
t = 6
t = T-4
t = T-2
t = T
…
…
t = 0
t = 2
t = 4
t = 6
t = T-4
t = T-2
t = T
Realignment
6-parameter rigid body registration & transformation
(Realign to the 1st volume)
→ 6 motion-related co-variates for fMRI analysis

## Slide 23: Realignment (Head motion correction)
Slice Timing Correction
Realignment
Segmentation
Co-registration
Normalization
Smooth
Data dependency
Volumes : EPI volumes after slice timing correction (a*.nii)

## Slide 24: Realignment (Head motion correction)
Slice Timing Correction
Realignment
Segmentation
Co-registration
Normalization
Smooth
Resliced images : All Images + Mean Image (mean*.nii)
Filename Prefix: create ra*.nii files after this step

## Slide 25: Segmentation (Bias field correction)
Slice Timing Correction
Realignment
Segmentation
Co-registration
Normalization
Smooth
Estimate tissue probability maps for each subject.
c1*.nii
(gray matter)
c2*.nii
(white matter)
c3*.nii
(CSF)
c4*.nii
(skull)
c4*.nii
(scalp)
Bias field correction → benefit for registration
Before correction
Bias field
After correction
(m*.nii)
Estimate deformation field
Subject space
Template
Deformation field
(y_*.nii)

## Slide 26: Segmentation (Bias field correction)
Slice Timing Correction
Realignment
Segmentation
Co-registration
Normalization
Smooth
Volumes : ~\HC003_20160620_CYJ\MRIData\T1\20*.nii
(1 volume)
Save Bias Corrected : Save bias corrected

## Slide 27: Segmentation (Bias field correction)
Slice Timing Correction
Realignment
Segmentation
Co-registration
Normalization
Smooth
Affine Regularisation : ICBM space template – East Asian Brains
Deformation Fields : Forward (subject T1 → template)

## Slide 28: Co-registration (cross-modality registration)
mean*.nii
Bias corrected T1 (m*.nii)
Slice Timing Correction
Realignment
Segmentation
Co-registration
Normalization
Smooth
Align fMRI (EPI) data to structural (T1W) image.
Matching modalities in individual subjects
Rigid body transformation using mutual information
T2*W EPI images
(low resolution & poor structural information)
T1W structural images
(high resolution)
Realigned EPI
(ra*.nii)
Deformation
matrix

## Slide 29: Co-registration (cross-modality registration)
Slice Timing Correction
Realignment
Segmentation
Co-registration
Normalization
Smooth
Reference Image : bias corrected T1W images (m*.nii)
Source Image : mean EPI volume (mean*.nii)
Other Images : intra-session realigned EPI volumes (ra*.nii)
* Fitting fMRI data (source image) to T1W structural images (reference image)
Data dependency
Match to Reference Image

## Slide 30: Normalization (native space → standard space)
Slice Timing Correction
Realignment
Segmentation
Co-registration
Normalization
Smooth
Apply deformation field
Deformation field
(y_*.nii)
Bounding box & origin
Bounding box (mm)
[-78 -112 -70
78 76 85]
Origin : anterior commissure (AC)
Voxel sizes [2 2 2] (mm)
Bias corrected T1 (m*.nii)
Co-registered EPI volumes
Deformation field
(y_*.nii)
Deformation field
(y_*.nii)
Normalized T1 (wm*.nii)
Normalized EPI volumes (wra*.nii)

## Slide 31: Normalization (native space → standard space)
Slice Timing Correction
Realignment
Segmentation
Co-registration
Normalization
Smooth
Data dependency
Deformation Field : forward deformation matrix (y_*.nii)
Images to write : co-registered EPI volume
Filename Prefix: create wra*.nii files after this step

## Slide 32: Normalization (native space → standard space)
Slice Timing Correction
Realignment
Segmentation
Co-registration
Normalization
Smooth
Data dependency
Deformation Field : forward deformation matrix (y_*.nii)
Images to write : bias corrected T1 volume (m_*.nii)
Filename Prefix: create wm*.nii files after this step

## Slide 33: Gaussian Spatial Smoothing
Slice Timing Correction
Realignment
Segmentation
Co-registration
Normalization
Smooth
Apply Gaussian kernel smoothing to the normalized EPI volumes
Each voxel becomes weighted average of surrounding voxels
Compensate for in accuracies in normalization between individuals
Increase signal-to-noise ratio (SNR)
FWHM (full width half maximum)
Mainly 5-10 mm FWHM (2 to 3 voxels)
Smoothing process may be skipped when the target brain region is small. (i.e. amygdala, deep nucleus)
(stamp)

## Slide 34: Gaussian Spatial Smoothing
Slice Timing Correction
Realignment
Segmentation
Co-registration
Normalization
Smooth
Data dependency
Images to Smooth : Normalized EPI volumes (wra*.nii)
FWHM : mainly 5-8 (mm)
Filename Prefix: create swra*.nii files after this step

## Slide 35: Analysis of Functional Magnetic Resonance Imaging (fMRI) Set up SPM Batch Jobs

## Slide 36: SPM Batch Jobs
>> spm fmri
> Batch
> BasicIO > Run > Run Batch Jobs
> fMRI_preprocessing_batch_YTLi20210112.mat
> Done

## Slide 37: SPM Batch Jobs
>> spm fmri
> Batch
> BasicIO > Run > Run Batch Jobs
> fMRI_preprocessing_batch_YTLi20210112.mat
> Done
Data folder
~\HC003_20160620_CYJ\MRIData\WM1
T1 files
~\HC003_20160620_CYJ\MRIData\T1\20*.nii
(1 volumes)
fMRI files
~\HC003_20160620_CYJ\MRIData\WM1\20*.nii
(105 volume)

## Slide 38: SPM Batch Jobs
>> spm fmri
> Batch
> BasicIO > Run > Run Batch Jobs
> fMRI_preprocessing_batch_YTLi20210112.mat
> Done
Save Generated Batch Jobs : Don’t Save
Missing Inputs : Don’t run any jobs if missing inputs

## Slide 39: SPM Batch Jobs
>> spm fmri
> Batch
> BasicIO > Run > Run Batch Jobs
> fMRI_preprocessing_batch_YTLi20210112.mat
> Done
Data folder
~\HC003_20160620_CYJ\MRIData\WM1
fMRI files
~\HC003_20160620_CYJ\MRIData\WM1\20*.nii
(105 volumes)
T1 files
~\HC003_20160620_CYJ\MRIData\T1\20*.nii
(1 volume)

## Slide 40: SPM Batch Jobs
>> spm fmri
> Batch
> BasicIO > Run > Run Batch Jobs
> fMRI_preprocessing_batch_YTLi20210112.mat
> Done
…
Create Batch Jobs for each subject!!!

## Slide 41: Check SPM processing logfile
SPM processing logfile (spm_Date.ps)
Convert *.ps file to *.pdf file (https://online2pdf.com/convert-ps-to-pdf)

## Slide 42: Analysis of Functional Magnetic Resonance Imaging (fMRI) General Linear Model (1st level analysis)

## Slide 43: fMRI Protocol (see DICOM tags)
(0008,0070) Manufacturer : SIEMENS
(0018,0087) Magnetic Field Strength : 3 (T)
(0008,1090) Manufacturer’s Model Name : Prisma
(0018,0024) Sequence Name : *epfid2d1_70 →2D GRE EPI
(0018,0080) Repetition Time : 2000 (ms)
(0018,0081) Echo Time : 20 (ms)
(0018,1314) Flip Angle : 90 (°)
(0028,0030) Pixel Spacing : 3\3 (mm)
(0028,0010) Rows : 64
(0028,0011) Column : 64
(0018,0088) Spacing Between Slices : 3.5 (mm)
(0018,0050) Slice Thickness : 3.5 (mm)
(0019,100A) Number of Image in Mosaic : 40 (slices)

## Slide 44: fMRI Protocol (experimental design)
N-back Verbal Working Memory Task (N = 1 or 2)

## Slide 45: General Linear Model (GLM)
Finding the linear combination of these hypothetical time series “best” fits the fMRI time series.

## Slide 46: General Linear Model (GLM) parameter estimation
Beta value represents the association between a condition design and the measured BOLD signal.

## Slide 47: General Linear Model (GLM) parameter estimation
Apply the same model to all voxels.
Different parameters (beta value) for each voxel.
Beta map for each task condition.

## Slide 48: Specify 1st-level Analysis Model
>> spm fmri
> Batch
> fMRI_1st_level_batch_YTLi20210112.mat
> Done

## Slide 49: Specify 1st-level Analysis Model
>> spm fmri
> Batch
> fMRI_preprocessing_batch_YTLi20210112.mat
> Done
Directory : create a new folder (i.e. ~\MRIData\WM1\1_back)
Units for design : Scans (*depends)
Interscan interval : (0018,0080) Repetition Time : 2000 (ms) → 2 (s)
Microtime resolution : (0019,100A) Number of Image in Mosaic : 40 (slices)
Microtime onset : 1 → Reference Slice

## Slide 50: Specify 1st-level Analysis Model
>> spm fmri
> Batch
> fMRI_preprocessing_batch_YTLi20210112.mat
> Done
Scans : ~\HC003_20160620_CYJ\MRIData\WM1\swra*.nii
(105 fMRI volumes)
Name : 1-back
Onsets : [16 46 76] (scans → depends on “Units for Design”)
Durations : 15 (scans for a stimulus block → depends on “Units for Design”)
Multiple regressors : head motion log file (r_p*.txt)

## Slide 51: Specify 1st-level Analysis Model
>> spm fmri
> Batch
> fMRI_preprocessing_batch_YTLi20210112.mat
> Done
Task condition
6 motion-related covariates
constant

## Slide 52: Estimate Model Parameters
>> spm fmri
> Results
> SPM.mat
> Done

## Slide 53: Estimate Model Parameters
>> spm fmri
> t-contrasts
> Define new contrast…
> Done
1_back
1 0 0 0 0 0 0 0

## Slide 54: Estimate Model Parameters
>> spm fmri
> apply masking : none
> threshold {T or p value} : none, 0.001
> & extent threshold {voxels} : 0
Model parameter (Subject level)

## Slide 55: Analysis of Functional Magnetic Resonance Imaging (fMRI) Group-Level Statistical Analysis (2nd level analysis)

## Slide 56: Statistical Inference on Group Data

## Slide 57: Specify 2nd-level Analysis Model : One-sample t-test
>> spm fmri
> Specify 2nd-level
Directory : create a new folder (i.e. ~\WM1_back_one_sample_t)
Scans : ~\MRIData\WM1\1_back\con_0001.nii

## Slide 58: Estimate Model Parameters
>> spm fmri
> Results
> SPM.mat
> Done

## Slide 59: Estimate Model Parameters
>> spm fmri
> t-contrasts
> Define new contrast…
> Done
WM1_back_one_sample_t
1

## Slide 60: Estimate Model Parameters
>> spm fmri
> apply masking : none
> threshold {T or p value} : none, 0.001
> & extent threshold {voxels} : 0
Model parameter (Group level)

## Slide 61: Specify 2nd-level Analysis Model : Two-sample t-test
>> spm fmri
> Specify 2nd-level
Directory : create a new folder (i.e. ~\WM1_back_two_sample_t_HC_mTBI)
Designs : Two-sample t-test
Group 1 Scans : ~\HC*\MRIData\WM1\1_back\con_0001.nii
Group 2 Scans : ~\mTBI*\MRIData\WM1\1_back\con_0001.nii

## Slide 62: Estimate Model Parameters
>> spm fmri
> Results
> SPM.mat
> Done

## Slide 63: Estimate Model Parameters
>> spm fmri
> t-contrasts
> Define new contrast…
> Done
WM1_back_two_sample_t_HC_mTBI
1 -1

## Slide 64: Estimate Model Parameters
>> spm fmri
> apply masking : none
> threshold {T or p value} : none, 0.001
> & extent threshold {voxels} : 0
Model parameter (Group level)

## Slide 65: Specify 2nd-level Analysis Model : Paired-sample t-test
>> spm fmri
> Specify 2nd-level
> Pairs > New: Pair (Subject Number)
Directory : create a new folder (i.e. ~\WM1_back_two_sample_t_HC_mTBI)
Designs : Paired t-test
Scans [1,2] : ~\1_back\con_0001.nii & ~\2_back\con_0001.nii

## Slide 66: Estimate Model Parameters
>> spm fmri
> Results
> SPM.mat
> Done

## Slide 67: Estimate Model Parameters
>> spm fmri
> t-contrasts
> Define new contrast…
> Done
WM2_1_back_pair_sample_t
-1 1

## Slide 68: Estimate Model Parameters
>> spm fmri
> apply masking : none
> threshold {T or p value} : none, 0.001
> & extent threshold {voxels} : 0
Model parameter (Group level)

## Slide 69: Analysis of Functional Magnetic Resonance Imaging (fMRI) Data Visualization

## Slide 70: Employed Software
Mango
  http://ric.uthscsa.edu/mango/download.html
xjview
  http://www.alivelearn.net/xjview/download/
bspmview
  https://www.bobspunt.com/software/bspmview/

## Slide 71: Thanks! 李宜恬 Yi-Tien Li, Ph.D. TMU Neuroscience Research Center, Taipei Medical University Translational Imaging Research Center, Taipei Medical University Hospital angela810727@tmu.edu.tw