## Slide 1: TMS原理與介紹
Basics
Hands-on
MP-Family

## Slide 2
The MagPro product line was first introduced in 1992 by MagVenture's sister company Tonica Elektronik
MagVenture A/S Lucernemarken 15 DK-3520 Farum Denmark
Phone: +45 4499 8444 Fax: +45 4439 0449

## Slide 3: History of Magnetic Stimulation
1896 Arsenne d‘Arsonval: used high power coils and showed that magnetic pulses induces phosphenes into human cortex
Silvanus P. Thompson: reproduced the results of d‘Arsonval
1985 Anthony Barker: First magnetic stimulator for clinical usage

## Slide 4
The first work of transcranial magnetoelectric stimulation (TMS) was puplished by Barker et al. in 1985
Since then, the technique of magnetic stimulation (MS) has been used in the study of both the central and the peripheral nervous system (Motor Evoked Potentials)
and starts to be used in therapy as a new treatment for major depressive disorder
(Repetitive Transcranial Magnetic Stimulation), and as an alternative to electroconvulsive therapy.
BioMag Laboratory
Helsinki University Central Hospital
with permission
Magnetic Stimulation

## Slide 5: Basics in Magnetic Stimulation
What is Magnetic Stimulation
How does it works?
Parameters
Safety regulations
MagPro-Family
Coil portfolio
Accessories

## Slide 6: A Magnetic Stimulator consists of two elements:
The “POWER Generator” - MagPro
The COIL which transfers the energy into the tissue
Different types of “power generators” are available for different applications.
Wide range of Coils for specific stimulations: Circular or 8, high or low focal, flat, parabolic or shaped, static or dynamic cooling.

## Slide 7: Magnetic Stimulation
Induced
EMF. Field
Charging Circuit
Output
Circuit
Tank
Capacitor
C
Power
Supply
V
COIL
Thyristor
Trigger
Capacitor is charged to 300 Joules (½ CV²)
Pulse triggers the thyristor
Thyristor discharges capacitor through the Coil
B
Which generates a magnetic field B ( 4 Tesla) and induces EMF field up to 50 KT/s
I
Current I :
Monophasic Biphasic

## Slide 8: Principle Functioning
Charging Circuit
continous charging of
tank capacitor (300 J)
Stimulation Circuit
Release of pulses based
on programed features
Power Generator
Coil
altered/pulsed coil current produces an altered/pulsed magnetic field.
This M-Field induces a counter running pulsed/altered E-Field

## Slide 9: Induced EMF Field
Depends on the geometry of the Coil
3.1T
70µs
Electric Field can be expressed in
V/m ( 100 V/m)
V/mm² ( 50mV/mm²)
kT/s ( 50 KT/s)
Initial Magnetic Gradient
(at surface of the coil)
3.1 / 70 • 10-6  44,300 T/s 44.3 kT/s
Total Magnetic Gradient (Biphasic)
|3.1 x 2| / 140 • 10-6  44.3 kT/s

## Slide 10: Monophasic or Biphasic Stimulus?
Clockwise positioned
Monophasic stimulus
Clockwise positioned,
induced current in tissue flows counterclockwise.
This preferentially activates right hemisphere,
i.e. left limb muscles,
and vice versa.
A biphasic stimulus does not show such preferential activation of either left or right hemisphere.
A biphasic stimulus generates a higher magnetic field B.
Biphasic stimulus

## Slide 11: Parameter
Intensity: Power provided by tank capacitor
Frequency: Pulses per second
Pulse type: mono-, biphasic, halfsine,
dI/dt: released current per pulse, sent through the coil
ISI/IPI: Inter Stimulus/Pulse Interval: time between the stimuli/pulses
ITI: Inter Train Interval: time between the trains (pause)
Burst: Pulses bundled to one stimuli
Twin: paired pulses, Pulse B in relation to Pulse A
Dual: paired pulses, Pulse A and B independent
MT: Motor Threshold
Train: No. of stimuli released with a dedicated frequency
Stimuli: defined pulse

## Slide 12: Coils
Power and focal of stimulation depend
on the geometry of the coil
Circular
Butterfly
The intensity of the electric field decrease with the square of the distance
Electric Field E
Coil
Magnetic Field B
With a Circular Coil, the electric field E is parallel to the plane of the coil.
Lines of E follow the shape of the coil.
With a Butterfly Coil, the electric field E is perpendicular to the plane of the coil and located under its centre.

## Slide 13: Coil Performance
At the surface of the coil
At 2 cm depth
Circular
Figure-8
(Butterfly)
Parabolic

## Slide 14: Coil Performance - Comparison

## Slide 15: Choice of Stimulating Coil
A B C
A coil warm-up with power and frequency rate of stimulation
Different coils will be used for:
single stimulation MEP - Cortical Excitability - Rehabilitation
low stressed stimulation Train of stimuli at 1pps (Static Fluid)
high stressed stimulation Train of stimuli at 10pps (Dynamic Fluid)

## Slide 16: Coil Orientation
Importance of the coil orientation with the figure-8 coil (butterfly).
Depending on the type of the coil, 45° orientation gives the highest response.
Roots

## Slide 17: Induced Current  Neuronal Depolarization
E
At  2cm in depth
Induced current  15-20 mA/µs
Electric field E:
50-60 V/m
10-20 mV/mm²
10-20 kT/s
Intracranial Field
E

## Slide 18: Waveform and Induced Electric Field
Biphasic
Typically chosen where high energy is needed with low power.
Application: MEP, rTMS and fMS
Monophasic
Used in brain research.
A large amount of energy is lost in the coil, which explains the faster heating of the coil and limits the number of stimulation.
Half Sine
Used in brain research.
Half sine waveform requires a small amount of energy compared with monophasic.
Biphasic Burst
Adjustable burst up to 5 pulses with selectable inter-peak interval.
Application: Theta-burst stimulation in long-term potentiation (LTP).

## Slide 19: Power Mode (+40%)
The power mode principle is to increase the duration of the pulse wave by adding capacitor of the MagOption unit. This results in increasing the quantity of energy by around 40%.
The benefit of this mode is to reduce the level of motor threshold versus the power output of the stimulator, expressed in true A/µs or by default in %.

## Slide 20: Paired-Pulses (Twin and Dual Mode w/ MagOption)
The Twin-pulse and Dual-pulse modes (also called paired-pulses) are techniques that use double magnetic stimulator. This is realized by using the “MagOption” unit. Two pulses are sent during the same shoot.
The delay between the two pulses (IPI) is adjustable up to 3,000ms.
In Dual mode two pulses have an independent power adjustment, up to 100%.
In Twin mode the second pulse is set as a ration of the first pulse (0.1 – 10)
Available waveforms in Twin and Dual modes: Biphasic, Monophasic and Half sine, depends on the MagPro model.
Applications:
Studies of the cortical excitability and plasticity.
The first pulse can activate both inhibitory and facilitator mechanisms, as well as modify the threshold and readiness of the second pulse.

## Slide 21: Coil’s Wirings (Small Inner Diameter)
Circular Coil
Butterfly Coil
Superimposed
Butterfly Coil
Parabolic Coil
Due to the complexity of multiple coils,
the magnetic gradient B/t is measured in 3 axis.

## Slide 22: Coil Focalization
Circular
Butterfly
Flat windings with a small inner diameter
Bulky windings with a large inner diameter
Peak Electric Field Strength
Radial Displacement from Centre, Parallel to the Coil Surface.
Windings
Windings

## Slide 23: Coil performance (with biphasic pulse)
Induced electric field
(100% Output Power)
Blue curve: measurements at the surface of the coil.
Red curve: measurements at 20mm in depth.

## Slide 24: Cool-Coil performance (with biphasic pulse)
± 3cm
Radial Distance
Blue: Surface of the coil
Red: 2cm above the coil
Induced electric field (100% Output Power)
Vertical Distance

## Slide 25: Cool-Coil performance (with biphasic pulse)
Sound Level at 10pps
Continuous stimulation
(Extrapolation)

## Slide 26: Magnetic Radiation
The magnetic field at one point is inversely proportional to the square of its distance from the coil.

## Slide 27: MagPro Family

## Slide 28: MagPro Family
MagPro Compact
MagPro R30
MagPro X100 with M.O
MagPro R100
MagPro R20

## Slide 29: MagPro Family - Routine
MagPro R20
stimulation frequency 1-20 Hz
biphasic waveform
documentation and report via WiFi
standard and static cooled coils
MagPro R30
stimulation frequency 0.1-30 Hz (80 Hz*)
biphasic waveform, (ThetaBurstStimulation*)
documentation and report via MS Excel*)
standard, static cooled and continuous cooled coils
upgradeable for advanced science
MagPro X100
stimulation frequency 0.1-100 Hz (250 Hz*)
biphasic/monophasic waveform, burst
documentation and report via MS Excel*)
standard, static cooled and continuous cooled coils
upgradeable for advanced science
* Optional items or packages, installable onsite

## Slide 30: MagPro Family - Research
MagPro X100 MO
stimulation frequency 0.1-100 Hz (250 Hz*)
biphasic/monophasic waveform, burst
paired pulses, half sine, Powerpulses
Paired pulse composer*)
Study-Mode for double blinded studies*)
documentation and report via MS Excel*)
standard, static cooled and continuous cooled coils
etc.
MagPro R30 MO
stimulation frequency 0.1-30 Hz
biphasic/monophasic waveform
paired pulses
Study-Mode for double blinded studies*)
documentation and report via MS Excel*)
standard, static cooled and continuous cooled coils
etc.
* Optional items or packages, installable onsite